e-MASS
Project Case Study

Table of Contents
# Project case study
In the process of applying a protective zinc coating to steel inhomogeneous coating is applied due to strip vibration. In inhomogeneous coating process hundred Tons of zinc wasted and also quality is reduced. To achieve the better quality need to apply homogeneous coating of zinc to steel plate. EMG introduced a system called electromagnetic strip stabilization system (e-MASS).
The electromagnetic strip stabilization system (eMASS) manufactured by EMG in Germany is a device for use in controlling the vibrations of steel strip in a non-contact manner through use of electromagnets and is in wide used all over the world.
It is installable on air knife units used to blow off any zinc attached to a steel strip in a zinc pot. The control device suppresses any vibration of the steel strip via the attraction of electromagnets and thus minimizes any quantity variations in the plated zinc.
# Task study
Gone through the USB-6218 data acquisition device from National Instruments understands about USB Multi function I/O Device and Hardware NI-9218.
The NI 9218 is a 2-channel, universal C Series module designed for universal measurements in NI Compact DAQ and Compact RIO systems.
The NI 9218 is ideal for creating universal test systems for automotive, off-highway, and data-logging systems.
USB and Ethernet interface for data feeding in to software.
Also gone through Transferring the text files to a SQL database in the background.

# FFT analysis
Gone through the FFT analysis of analog signal, Sum, differential signals and plotting of the signals.
# Data recording
Primary concern for the data recording is data measurement and data security, measured data must be lossless and stored in to the files.
Gone through data recording and Zipping operation performed into the file on every 1 min interval.
Data recording configuration can be set based on file size or time interval.
By using the above features can achieve the hard disk capacity of 500GB and can store the data approx. 700 days.
The recording process can be paused or resumed in a manual or condition-based manner.
# General improvement and enhancements
Gone through several windows displayed simultaneously also performed operations related to data stored in configuration files and default files.
Reload configurations from backup files and managed project directory by mapping the drive.

# Report generation
As per above data recording file is generated we generate pdf analysis report of that file.